Description of Device.

Tom Thumb

Generic name of device: Infant Resuscitation Unit.
Model name: Tom Thumb
Model numbers: TT480, TT490, TT495 Family’s
Part numbers: 0310xxx

The Tom Thumb is an infant resuscitation unit, designed to replace the manual ventilation by the bag, mask and valve method.

It is intended for use in emergency resuscitation situations such as delivery rooms, operating theatres and special baby care units.

It is designed to control a flow of gas from an external source. The flow being controlled, by the operator occluding one leg of a Tee on the mask, instead of the original and usually uneven method of bag compressions.

The Tom Thumb is available in several models depending on the gas source.