Microstim Electrodes

The Microstim delivers an electric pulse to the skin. It is immaterial how the device is connected. It can be dumbbells, two wires taped to the skin or ECG electrodes.

ECG electrodes were chosen because they were readily available in most clinical areas and are very familiar to staff. They are easy to use and offer consistent application.

They were chosen in preference to Dumbbells because dumbbells only present a very small surface area and need to be used with extreme care. Intermittent contact can cause pain or distress to the patient.

The Microstim can function adequately with two bare wires.

Due to its design, it is reasonable to cope with small variations in patient skin impedance. It is designed to work on the universally accepted nominal around 1 KΩ. The use of ECG electrodes reduces poor contact problems.

The function and efficacy of ECG electrodes is well documented as is they are universally used on ECG and patient monitoring equipment.

John S Lamb
20/09/17