NB for purposes of test the client must declare which category of each of the following classes the equipment has been designed to meet			Class
Power source	Mains Operated	Specify voltage range and frequency
		Specify rated input power and power source
	Internal electric power source
	Equipment supplied from a specified power source
Type of protection against electric shock	Class1 ; mains supplied equipment using a protective earth
	Class II ; mains supplied equipment without a protective earth ( double insulated)
	Internally powered equipment
Mode of operation	Continuous- equipment may be left switched on indefinitely
	Short time – equipment may only be used for a defined time followed by a long cooling period
	Intermittent- equipment may only be used for a defined time followed by a rest period- define the duty cycle
	Continuous with short time loading
	Continuous with intermittent loading define the duty cycle
Degree of protection against ingress of liquids	Not protected
	Drip proof -protected against dripping water
	Splash proof -protected against splashing water
	Watertight -protected against total submission
Degree of mobility	Fixed-equipment in specific location
	Permanently installed-equipment which may be moved from one location to another on its own wheels or similar
	Portable- equipment intended to be moved from one location to another by being carried.
	Hand-held- equipment supported by handduring normal use
Degree of protection against electric shock	Type B- equipment without an Applied part or with an applied part not designed to meet F type (Floating) requirements
	Type BF- equipment with an F-Type Applied part
	Type CF- equipment with an F-Type Applied part having a higher degree of protection than for a Type BF equipment and primarily intendedfor direct cardiac applications
Degree of protection against flammable anaesthetic mixtures	Not protected
	AP- designed to avoid sources of ignition within 5cm to 25cm of enclosure
	APG- designed to avoid sources of ignition within 5cm of enclosure

NB The followingdata and samples must be supplied at the same time as the equipment is submitted and may not be returned after testing.]

1. Operators Manual	2. Service Manual
3. Circuit diagrams	4. Mains transformer

Other components and information may be needed. These can be only be defined following the initial examination of the unit