## Slide 1
MDR Introduction, Structure, Timelines and Implementation
Damon Williams
Business Development Manager - BSI

## Slide 2
Wider scope of medical devices / updated classifications
Stronger supervision of independent assessment bodies by national authorities
More powers for assessment bodies for a thorough assessment
Clearer rights & responsibilities for various economic operators
Extended Eudamed database on medical devices
Better traceability of medical devices
Stricter requirements for clinical evidence
Better coordination between various entities
MDR/IVDR are a major revision to MDD+AIMDD/IVDD
Significant Impact on
Manufacturers
Notified Bodies
Competent Authorities
EU commission
MDR/IVDR - Goals of the Commission*

## Slide 3
MDR – (EU) 2017/745
Recitals – 101 ‘Whereas’ statements which justify the adoption of the Regulation
Chapter I – Scope and definitions (Articles 1 – 4)
Chapter II – Making available on market, Economic Operators (Articles 5 – 24)
Chapter III – Identification, Traceability and Registration of devices and Economic Operators (Articles 25 – 34)
Chapter IV – Notified Bodies (Articles 35 – 50)
Chapter V – Classification & Conformity Assessment (Articles 51 – 60)
Chapter VI – Clinical Evaluation & Clinical Investigations (Articles 61 – 82)
Chapter VII – PMS, Vigilance and Market Surveillance (Articles 83 – 100)
Chapter VIII – Co-operation (Articles 101 – 108)
Chapter IX – Confidentiality, Data Protection, Funding and Penalties (Articles 109 – 113)
Chapter X – Final Provisions (Articles 114 – 123)
Annex I – General Safety and Performance Requirements
Annex II – Technical Documentation
Annex III – Technical Documentation on PMS
Annex IV – EU DoC
Annex V – CE marking of conformity
Annex VI – Information for registration of devices and Economic Operators
Annex VII – Requirements to be met by NBs
Annex VIII – Classification Rules
Annex IX – Conformity Assessment – QMS and Technical
Annex X – Conformity Assessment – Type examination
Annex XI – Conformity Assessment – Product conformity verification
Annex XII – Certificates issued by a NB
Annex XIII – Custom-made Devices
Annex XIV – Clinical Evaluation and PMCF
Annex XV – Clinical Investigations
Annex XVI – Products without an intended Medical Purpose
Annex XVII – Correlation table
Structure of the Regulations

## Slide 4
Transition Timelines
MDR & IVDR

## Slide 5: MDR Transition (Article 120)
Adoption of MDR
05 May 2017
Entry in to Force
25 May 2017
NBs designation
under MDR
Date of Application
26 May 2020
MDD/AIMDD certificate validity
(4 years )
MDD/AIMDD certificates can be issued/re-issued/renewed
MDR certificates
Transition period
3 years
MDD/AIMDD Annex IV certificates void on 27 May 2022
No more « making available or putting into service » of devices covered by MDD/AIMDD certificates
MDD/AIMDD certificates void
27 May 2024
27 May 2025
NBs can apply for designation
26 Nov 2017
Notes: Exception: Annex 4 (no validíty dates – void on 27th of may 2022)

## Slide 6: Transition timelines
Important points
After 26 May 2020, devices certified under MDD/AIMDD (26 May 2022 for devices certified under IVDD) can only be placed on market if:
  They continue to comply with applicable Directives
  There are no significant changes in the design and intended purpose
  However, following MDR/IVDR requirements will apply
    post-market surveillance,
    market surveillance,
    vigilance,
    registration of economic operators
    registration of devices

## Slide 7
Delegated & Implementing Acts: MDR & IVDR

## Slide 8
Allows focus on policy and direction without getting lost in the detail
Faster to agree and publish legislation
Allows to learn from experience
There is legal precedent – Treaty on the functioning of the EU (TFEU or 2012/C 326/01)
Why adopt Delegated and Implementing Acts?

## Slide 9
Delegated Acts
Acts used to modify/amend the ‘What’ of a legislation, but limited to the non-essential elements of that legislation.
Implementing Acts
Acts which are used to clarify/implement the ‘How’ of a legislation
Additional References:
http://eur-lex.europa.eu/legal-content/EN/TXT/?uri=uriserv%3Aai0032
http://eur-lex.europa.eu/summary/glossary/norms_hierarchy.html
http://eur-lex.europa.eu/summary/glossary/norms_hierarchy.html
http://www.eipa.eu/files/repository/product/20130904094203_Comitology_Brochure5EN_web.pdf
http://www.clientearth.org/reports/introduction-to-delegated-and-implementing-acts.pdf
What do they mean (in normal English)…

## Slide 10
MDR Scope

## Slide 11: European Medical Device Regulations 2017/745 Scope
In:
Medical Devices from 93/42/EEC (Recital 6)
Active Implantable Medical Devices from 90/385/EEC (Recital 6)
medical devices incorporating (non-viable) human tissues (Recital 11)
devices similar to medical devices, but without a medical purpose (Recital 12)
Notes: All devices covered by mdd / aimd, meddev with human tissue (non-viable), close to meddevs without medical purpose (contact lenses)

## Slide 12: European Medical Device Regulations 2017/745 Scope
In:
in vitro diagnostics
medicinal products
cosmetics
food
products containing viable tissues or cells of human or animal origin (Recital 13)
Out (largely unchanged):
(Recital 7)
Clarification – Article 1(6h):
Devices incorporating viable biological materials or organisms (including bacteria, fungi, viruses) are excluded
Medical Devices from 93/42/EEC (Recital 6)
Active Implantable Medical Devices from 90/385/EEC (Recital 6)
medical devices incorporating (non-viable) human tissues (Recital 11)
devices similar to medical devices, but without a medical purpose (Recital 12)

## Slide 13: European Medical Device Regulations 2017/745 Scope
In:
in vitro diagnostics
medicinal products
cosmetics
food
products containing viable tissues or cells of human or animal origin (Recital 13)
Out (largely unchanged):
(Recital 7)
Clarification - Recitals 8, 9:
MS to decide on case by base basis for borderline products, including those incorporating biological substances, medicinal products, and those which could be considered cosmetics, food products or biocides. Commission may intervene to ensure consistency, in coordination with MDCG, EMA, European Chemicals Agency or European Food Safety Authority
Medical Devices from 93/42/EEC (Recital 6)
Active Implantable Medical Devices from 90/385/EEC (Recital 6)
medical devices incorporating (non-viable) human tissues (Recital 11)
devices similar to medical devices, but without a medical purpose (Recital 12)

## Slide 14: European Medical Device Regulations 2017/745 Scope
In:
Clarification - Article 1(10):
Devices incorporating human derived substances are not within the scope of the Regulation if the action of these substances is principal and not ancillary to that of the device. These products will be governed by Directive 2004/23/EC EU Tissues and Cells Directive)
Medical Devices from 93/42/EEC (Recital 6)
Active Implantable Medical Devices from 90/385/EEC (Recital 6)
medical devices incorporating (non-viable) human tissues (Recital 11)
devices similar to medical devices, but without a medical purpose (Recital 12)

## Slide 15: European Medical Device Regulations 2017/745 Scope
In:
Clarifications - Article 1(3):
For devices without a medical purpose, Commission should develop common specifications, at least regarding risk management and (where necessary) clinical evaluations for safety (Article 1(2))
If devices have both medical and non-medical purpose, they must meet requirements for both
Medical Devices from 93/42/EEC (Recital 6)
Active Implantable Medical Devices from 90/385/EEC (Recital 6)
medical devices incorporating (non-viable) human tissues (Recital 11)
devices similar to medical devices, but without a medical purpose (Recital 12)

## Slide 16: European Medical Device Regulations 2017/745 Scope
In:
Clarifications – Recital 19:
Software with a medical purpose is a medical device
Software with lifestyle or well-being purposes is not a medical device – even if used in a healthcare setting
Medical Devices from 93/42/EEC (Recital 6)
Active Implantable Medical Devices from 90/385/EEC (Recital 6)
medical devices incorporating (non-viable) human tissues (Recital 11)
devices similar to medical devices, but without a medical purpose (Recital 12)

## Slide 17
Overview, Annex I General Safety and Performance Requirements

## Slide 18: Differences: Regulation GSPRs vs Directive ERs
  Overall Structure and Trends:
    Some numbering and organizational changes
    Overall similar content and topics (some title changes: i.e. construction  manufacturing)
    Expanded requirements (Labeling, Risk)
    New areas of emphasis (from standards and guidances, etc.)
    Some additional requirements because of merging of MDD with AIMDD
    Some topics move out of the SPR list into Articles/Annexes (Clinical, medicinal consultation)
  Some new topics introduced (devices without medical purpose, lay person use, etc.)
MDD : 13 Essential requirements
AIMD : 16 Essential requirements
MDR :
23 Safety & Performance requirements

## Slide 19: MDR Annex I: General Safety and Performance Requirements
Chapter 1: General Requirements
(SPRs 1-9)
Chapter 2: Design and Manufacture
(SPRs 10-22)
Chapter 3: Information Supplied with the Device
(SPR 23)

## Slide 20: Annex I – Safety & Performance Requirements
Safe, Perform as Intended, State of the Art
Risk Reduction as far as possible
Risk Management
Risk Control
Risk of Use Error
Lifetime
Packaging, Transport, Storage
Undesirable Side-effects Minimised & Risks<Benefits
20

## Slide 21: Annex I – Safety & Performance Requirements
For the devices referred to in Annex XVI, the general safety requirements set out in Sections 1 and 8 shall be understood to mean that the device, when used under the conditions and for the purposes intended, does not present a risk at all or presents a risk that is no more than the maximum acceptable risk related to the product's use which is consistent with a high level of protection for the safety and health of persons.
Common Specification
21

## Slide 22: Annex I – Safety & Performance Requirements
Chemical, Physical & Biological Properties
Infection & Microbial Contamination
Devices incorporating a medicinal product and devices composed of substances that are absorbed by or locally dispersed in the human body
Devices incorporating materials of biological origin
Construction and interaction with the environment
Devices with a diagnostic or measuring function
Protection against radiation
22

## Slide 23: Annex I – Safety & Performance Requirements
Electronic programmable systems
Active devices and devices connected to them
Requirements for Active Implantable Devices
Protection against mechanical and thermal risks
Protection against the risks posed to the patient or user by supplied energy or substances
Protection against the risks posed by medical devices intended by the manufacturer for use by lay persons
23

## Slide 24: Annex I – Safety & Performance Requirements
Labels and Instructions for Use
24
(a)
(b)
(c)
(d)
(e) medicine, human, animal
(f) CMR + ED >0.1%
(g)
(h)
(i)
(j)
(k)
(l)
(m)
(n)
(o) reprocessing cycles
(p) custom made
(q) clinical investigation
(r) quantity of constituents – achieving principal intended action
(s)
Article 18 – Implant Card
Article 20

## Slide 25: Clinical Evaluation Snapshot of changes

## Slide 26: Snapshot of changes
Consultation and Scrutiny procedures for Class III implantable and Class IIb active drug delivery / removal devices (Articles 54 and 55 – more detail on next slides)
Product certificates required for Class IIb implantable devices (except sutures, staples, dental fillings, dental braces, tooth crowns, screws, wedges, plates, wires, pins, clips and connectors) (Article 52(4))
Depth of technical documentation assessment (including clinical evaluation) no longer based on device risk classification? (Article 52; Annex IX or X)
Clinical Evaluation Assessment Report (CEAR) to be provided to manufacturer as part of the technical documentation assessment for all device classifications (Article 52; Annex IX or X)
Greater emphasis on use of clinical experts in clinical evaluation assessments (Article 52; Annex IX or X; Annex VII)
NB to document requirements for interim review of PMCF outputs throughout certification period (Article 52; Annex IX or X)

## Slide 27: Snapshot of changes
Applies to Class III implantable devices and Class IIb active device intended to administer or remove a medicinal product
Does not apply to:
  Certificate renewals
  Design modifications where manufacturer satisfactorily demonstrates to NB that risk-benefit ratio is unaffected
  Clinical evaluation CS exists for that device type, and NB confirms that the CER meets CS requirements
Clinical evaluation consultation procedure (Chapter V, Article 54)
Article 54(3):
NBs must notify CAs and Commission through EUDAMED of decision of whether or not this consultation is to be applied
Notification shall be accompanied by CEAR

## Slide 28: Clinical evaluation consultation procedure (Article 55)
Manufacturer’s Clinical Evaluation
NB Clinical Evaluation Assessment Report
PMCF Plan
Restrict indications
Limit duration of certificate
Undertake specific PMCF studies
Adapt IFU or Summary of Safety and Clinical Performance
Impose other restrictions
Class III Implant or Iib active drug delivery
EU Commission
NB Further Review
Complete Conformity Assessment
21 days
Notified Body Review
Notified Body Review
39 days
Benefit:Risk Determination
Consistency with indications
PMCF Plan
No ‘scientific opinion’
Notified Body Certificate
Notified Body Certificate
NB must justify if expert panel advice not followed

## Slide 29: Requirements for SSCP
Requirements defined:
Article 32 (Summary of safety and clinical performance)
SSCP required for Class III and implantable devices
Draft submitted as part of the application for certification to NB
Identifies device, intended use, safety and performance characteristics and summary of technical and clinical evidence of conformity
Updated whenever PMS data affects conclusions (Article 62(11))
Validated by NB and made available to the public via Eudamed
Requirements for content may be amended by implementing acts
Notes: For IVD: SSP – Summary of Safety Performance (class D + C compaignion Diagnostics) ?

## Slide 30
Overview of Key Technical Documentation Requirements

## Slide 31: MDR/IVDR Requirements for technical documentation
Highlights:
General requirements similar to Directives, but content more explicitly defined in Annex II
Dedicated Annex (III) for Technical Documentation on Post-market surveillance
Periodic Safety Update Reports and Summary of Safety and Clinical Performance (or Summary of Safety and Performance for IVDs) specified as part of the Technical Documentation
Annexes II and III of the Regulations do not follow IMDRF suggested Table of Contents for technical documentation

## Slide 32: MDR/IVDR Requirements for technical documentation
1: Device description
2: Information to be supplied by the manufacturer
3: Design and manufacturing information
4: General safety and performance requirements
6: Product verification and validation
5: Benefit-risk analysis and risk management
Annex III: Technical Documentation on Post-Market Surveillance
Annex II: Technical Documentation
+ PSUR (MDR & IVDR)
+ SSCP (MDR)
+ SSP (IVDR)

## Slide 33: MDR/IVDR Requirements for technical documentation
1: Device description
2: Information to be supplied by the manufacturer
3: Design and manufacturing information
4: General safety and performance requirements
6: Product verification and validation
5: Benefit-risk analysis and risk management
Annex III: Technical Documentation on Post-Market Surveillance
Annex II: Technical Documentation
Technical Documentation
Annexes II and III
Traceability
Chapter III
Safety and Performance
Annex I
Conformity routes
Annexes IX - XI
Clinical Evaluation
Chapter VI, Annex XIV
Clinical Investigation
Chapter VI, Annex XV
Postmarket Surveillance, PSUR and vigilance
Chapter VII
Notes: Intention here is to say that, although the requirements for Technical Documentation are outlined in Annexes II and III of the MDR and IVDR, lots of other Chapters and Annexes feed into this (the ones listed on this example are from the MDR rather than IVDR)

## Slide 34: Conformity Assessment – EU Regulation
Year 1
Year 2
Year 3
Year 4
Year 5
Initial (Stage 1 & 2)
Continuing Assessment
Continuing Assessment
Re-assessment
Microbiology
Microbiology
Technical Documentation
Continuing Assessment
Continuing Assessment
Technical Documentation
Unannounced Audit
Unannounced Audit
34
PSUR – Implantable, Class III
PSUR – Implantable, Class III
PSUR – Implantable, Class III
PSUR – Implantable, Class III
Microbiology

## Slide 35: Existing client MDR Transitions

## Slide 36: Existing Client Transitions (Proposed as per MDP4200 draft)
36
All manufacturers currently certified by BSI have to lodge a new application to the Regulations
QMS Transition
Initial Assessments can be combined with any scheduled audit plus any additional time as shown below.
Technical Documentation
Review durations to range from 2-7 days. Sampling allowed for IIa and IIb non-implantable devices.
Microbiology Transition QMS certification: No additional time for manufacturers who received an M audit in the last 3 year Product Specific certification: Class IIb implants may require Microbiologist review of Technical Documentation

## Slide 37: New Manufacturer - MDR Applications

## Slide 38: Initial applications – New Manufacturers – QMS & Micro
38
QMS & Micro audits: Same principles as before

## Slide 39: Initial applications – New Manufacturers – Technical
39
Classification MDR | Technical Documentation Review MDR | Guidance on Duration* (per file)
Class III custom made implantable | None | None
Class Is, Im | None | None
Class Ir | None | None
Class IIa | One sample from each category | 2-3 days
Class IIb | One sample from each generic device group | 3 days
Class IIb, active intended to administer medicines | One sample from each generic device group + Clinical evaluation consultation | 3 days
Class IIb implantable | All | 3-4 days
Class III | All | 8-10 days
Class III – Rule 14 and/or 18 | All + Med/AT consultation | 8-10 days (excluding consultation)
Class III implantable | All + Med/AT consultation (if applicable – Rule 14 and/or 18) + Clinical evaluation consultation | 8-10 days (excluding consultation + clinical evaluation consultation)
(Draft MDP4200)

## Slide 40: Regulation EU 2017/745 – Conformity Assessment
 | Quality Management System | Microbiology | Technical Documentation | Unannounced Audit | Clinical Evaluation Consultation Procedure (CECP) (Article 54) | 2001/83/EC EC/726/2004 2004/23/EC EU 722/2012 | PSUR (Article 86) (*Annual) | SSCP (Article 32)
Class III Implants |  |  |  |  5 years |  |  | * | 
Class III |  |  |  |  5 years |  |  | * | 
Class IIb Active Intended to administer and/or remove Medicines from the body |  |  | Sample per group |  5 years |  |  | * not submitted to NB | 
Class IIb Implants |  |  |  |  5 years |  |  | * | 
Sutures, staples, dental fillings, dental braces, tooth crowns, screws, wedges, plates, wires, pins clips, connectors |  |  | Sample per group |  5 years |  |  |  | 
Class IIb |  |  | Sample per group |  5 years |  |  | * not submitted to NB | 
Class IIa |  |  | Sample per category |  5 years |  |  |  not submitted to NB | 

## Slide 41: Regulation EU 2017/745 – Conformity Assessment
 | Quality Management System | Microbiology | Technical Documentation | Unannounced Audit | Clinical Evaluation Consultation Procedure (CECP) (Article 54) | 2001/83/EC EC/726/2004 2004/23/EC EU 722/2012 | PSUR (Article 86) (*Annual) | SSCP (Article 32)
Class Is, Im, Ir |  |  |  |  5 years |  |  |  | 
Class I |  |  |  |  |  |  |  | 
Class III Custom Made Implants |  |  |  |  5 years |  |  |  | 
Custom Made |  |  |  |  |  |  |  | 
Procedure Packs (Article 22) |  |  |  |  5 years |  |  |  | 
Suppliers, Subcontractors |  *depends on certification held |  *depends on certification held |  |  5 years |  |  |  | 
EU Authorised Representatives, Importers, Distributors (Article 16) | *impact sterile barrier, translate, repackage | *impact sterile barrier, translate, repackage |  |  5 years |  |  |  | 
Drug Delivery Products (Article 117) |  |  | *conformity with SPRs |  |  |  |  | 

## Slide 42: Any questions? Q&A Session later